## Slide 1: Rescue on Wheels Workshop – week 2 Ruud Slokker

## Slide 2: topics
Raspberry pi camara
Pull down and pull up resistors

## Slide 3: Pi –Camera - raspistill
Pictures: raspistill
Example:
raspistill -w 640 -h 480 -q 5 -o /tmp/pic.jpg &
-q: quality range [0, 100]
&: running in the background
Video: raspivid
example:
raspivid -fps 25 -o myvideo.h264 -t 10000
This will record 10 seconds of video.

## Slide 4: Pi –Camera – raspistill [2]
raspistill
raspistill –t 1000 mypicture.jpg
-t is the delay in milliseconds before the image is taken after you press Enter.
To take a sequence of pictures as a timelapse sequence the command is:
raspistill -t 900000 -tl 30000 -o mypicture%d.jpg
-t total time for sequence, 90000 ms = 15 min
-tl how often to take a picture. 30000 ms = 30 seconds
%d = picture number. output would be mypicture1.jpg mypicture2.jpg mypicture3.jpg

## Slide 5: Pi –Camera – raspistill [3]
raspistill
raspistill –ss 300 -n mypicture.jpg
-ss = shutter speed; max = 6000
-n = no preview
raspistill –ex sports mypicture.jpg
-ex = exposure mode //sports : fast shutter
raspistill –md 2 mypicture.jpg
-md = mode
mode 2: 2592x1944; mode 6: 640x480

## Slide 6: Field of view
Describe the relation between the field of view and the focal length of the camera lens.

## Slide 7: MOTIONBLUR
How can motion blur be reduced?

## Slide 8: ASSIGNMENTS
Make use of:
http://www.raspberrypi.org/wp-content/uploads/2013/07/RaspiCam-Documentation.pdf
1a Make a picture of an object with the rasp. pi camera.
1b Make a video of an object with the rasp. pi camera.
Take a picture of a moving object. Reduce the motion blur of the pi-camera by reducing the
shutter time.
Take a picture of some text and apply the ocr-function on the
raspberry pi on the image:
http://www.instructables.com/id/BrickPi-Bookreader-Digitize-Books-With-Mindstorms-/step7/Installing-the-Optical-Character-Recognition-OCR-E/

## Slide 9: PULL UP/ Down resistors
Problem without pull up / down resistor
microcontroller
input pin
gnd
noise source
noise voltage on the input pin

## Slide 10: PULL UP resistors
microcontroller
input pin
gnd
Internal pull up resistor
microcontroller
input pin
gnd
external pull up resistor
Wiring pi library:
pullUpDnControl(0,PUD_UP);

## Slide 11: PULL DOWN resistors
microcontroller
input pin
gnd
Internal pull down resistor
Wiring pi library:
pullUpDnControl(0,PUD_DOWN);
noise source
Noise voltage on the input pin is strongly reduced by a pull down
(or pull up) resistor.